## Slide 1
ACCESSORIES & KIT

## Slide 2
November 2013
Availability

## Slide 3
e.sywall – bracket for wall installation

## Slide 4
e.sywall – bracket for wall installation
e.sybox is already set up for installation hanging on the wall with the DAB accessory kit e.sywall.
Advantages:
Saving space on the ground
Possibility to simultaneously connect 2 different deliveries in vertical position

## Slide 5
e.sydock – fast connection tool kit
Notes: 5
5

## Slide 6
e.sydock – fast connection tool kit
Accessory kit for Quick Connection of the system. This is a quick coupling base on which to make the connections to the plant and from which the system can be simply connected or disconnected.
Advantages:
possibility of making up the plant on-site, testing it, but removing the actual system until the moment of delivery, avoiding possible damage
it is easy for the assistance service to replace the system with a “spare” in the event of special maintenance
Notes: 6
6

## Slide 7
e.sydock – connection features
1 upper covers
4 Clammers: to fasten the union + side plugs
2 suction and delivery union
2 side plugs
2 adapters:
to connect the e.sybox

## Slide 8
e.sydock – suction and delivery on one side
Delivery
Suction
Closed Side
Delivery
Suction
Closed Side
Right Suction and Delivery
Left Suction and Delivery
FRONT
FRONT

## Slide 9
e.sydock – suction and delivery in line
Delivery
Suction
Closed Side
Closed Side
Delivery
Closed Side
Closed Side
Suction
Left Suction, Right Delivery
Right Suction, Left Delivery
FRONT
FRONT

## Slide 10
e.sydock – hydraulic connection fixing
WARNING:
Use the quick guide during the installation
Pay attention on the correct position of all o-rings
Grease all o-rings before placing them

## Slide 11
e.sytwin – booster set

## Slide 12
Pump set made up of two pumps whose deliveries all flow into a common manifold (pumps in parallel).
Advantages:
Increasing hydraulic performance in comparison with a single device
Ensuring continuity of operation in the event of a device developing a fault
Sharing out the maximum power
Wireless communication:
Modules communicate each other without any cable, just using the wireless connection unit placed on the inverter.
e.sytwin – booster set

## Slide 13
e.sytwin – booster set

## Slide 14
Performance curves of the complete e.sytwin unit including all the connections
(for vessel, heat sink, inverter controllers, check valve, flow and pressure sensors)
e.sytwin – performance
2 Pump Full Speed

## Slide 15
Chart: Q (l/min)
| 147 | 146 | 140 | 123 | 106 | 90 | 73 | 73 | 67 | 50 | 33 | 17 | 0
set point 4bar | 3.138 | 3.1 | 2.87 | 2.58 | 2.34 | 2.18 | 2 | 1.55 | 1.32 | 1.03 | 0.79 | 0.63 | 0.45
set point 3bar | 3.138 | 3.1 | 2.67 | 2.36 | 2.16 | 1.95 | 1.8 | 1.55 | 1.12 | 0.81 | 0.61 | 0.4 | 0.25
set point 2,5bar | 3.138 | 3.1 | 2.48 | 2.23 | 2.05 | 1.9 | 1.79 | 1.55 | 0.93 | 0.68 | 0.5 | 0.35 | 0.24
Twin | 3.138 | 3.138 | 3.138 | 3.138 | 3.138 | 3.138 | 3.138 | 3.138 | 3.138 | 3.138 | 3.089 | 2.826 | 2.441 | 1.829
2200 Watt at 4 bar 1860 Watt at 3 bar 1800 Watt at 2,5 bar with 8 X Open (96 l/min)
ENERGY SAVING AREA
2 Pump Full Speed
e.sytwin – energy saving
Thanks to the Inverter technology, e.sybox draws only the necessary energy according to water requirements, thereby avoiding wastes and allowing considerable economic savings.

## Slide 16
Chart: Q (l/min)
| 147 | 146 | 140 | 123 | 106 | 90 | 73 | 73 | 67 | 50 | 33 | 17 | 0
set point 4bar | 3.138 | 3.1 | 2.87 | 2.58 | 2.34 | 2.18 | 2 | 1.55 | 1.32 | 1.03 | 0.79 | 0.63 | 0.45
set point 3bar | 3.138 | 3.1 | 2.67 | 2.36 | 2.16 | 1.95 | 1.8 | 1.55 | 1.12 | 0.81 | 0.61 | 0.4 | 0.25
set point 2,5bar | 3.138 | 3.1 | 2.48 | 2.23 | 2.05 | 1.9 | 1.79 | 1.55 | 0.93 | 0.68 | 0.5 | 0.35 | 0.24
Twin | 3.138 | 3.138 | 3.138 | 3.138 | 3.138 | 3.138 | 3.138 | 3.138 | 3.138 | 3.138 | 3.089 | 2.826 | 2.441 | 1.829
ENERGY SAVING AREA
2 Pump Full Speed
3190 Watt at 4 bar 2800 Watt at 3 bar 2440 Watt at 2,5 bar with 4 X Open (160 l/min)
Thanks to the Inverter technology, e.sybox draws only the necessary energy according to water requirements, thereby avoiding wastes and allowing considerable economic savings.
e.sytwin – energy saving

## Slide 17
Caps to discharge the system in case of maintenance/removal of the e.sybox
Delivery & Suction Unions
Side caps
Anti Vibration Feet
Ground Fixing System
e.sytwin – features

## Slide 18
e.sytwin – connection features
4 Clammers: To fix the central junction.
2 upper covers
4 Clammers: to fasten the union + side plugs
2 suction and delivery union
2 side plugs
4 adapters: to connect 2 e.sybox
2 maintenance plugs: see next slide

## Slide 19
e.sytwin – suction and delivery on one side
Delivery
Suction
Closed Side
Delivery
Suction
Closed Side
Right Suction and Delivery
Left Suction and Delivery
FRONT
FRONT

## Slide 20
e.sytwin – suction and delivery in line
Delivery
Suction
Closed Side
Closed Side
Delivery
Closed Side
Closed Side
Suction
Left Suction, Right Delivery
Right Suction, Left Delivery
FRONT
FRONT

## Slide 21
WARNING:
Use the quick guide during the installation
Pay attention on the correct position of all o-rings
Grease all o-rings before placing them
e.sytwin – hydraulic connection fixing

## Slide 22
e.sytwin – wireless connection
NO CABLE INTERCONNECTION BETWEEN E.SYBOX

## Slide 23
It’s possible to disconnect one e.sybox ensuring the water supply thanks to the remaining e.sybox (left pic.).
After disconnecting one unit, fix the adapters and the upper cover to the base. Then screw the 2 maintenenace plugs to the adapters.
e.sytwin – connection features

## Slide 24
882
540
755
TOTAL VOLUME ≈ 190 dm3
- 50% of occupied space
710
750
350
e.sytwin – compact
TOTAL VOLUME ≈ 360 dm3
Pressure vassel not included

## Slide 25
e.sybox accessories – code & dimensions
 | Code | Dimensions [mm] | Dimensions with e.sybox [mm]
 | 60161442 | 185L x 25P x 144H | -
 | GAS – 60147247 | 293L x 318P x 180H | 293L x 345P x 679H (with 1 e.sybox installed)
 | NPT – 60150514 |  | 
 | GAS – 60160491 | 752L x 358P x 230H | 752L x 358P x 730H (with 2 e.sybox installed)
 | NPT – 60162081 |  | 
* e.sybox not included (to order : cod. 60147200 )

## Slide 26
THANK YOU FOR YOUR ATTENTION